Remote Control of host
ggg.instigate.training

---
Agenda: Network services
- SSH
- Telnet
- VNC

---
SSH
SSH (Secure shell) is a program which allows to connect to remote host via encrypted channel. It can be used for accessing shell on the remote computer as well as executing single commands on remote computer.
Syntax: ssh [options] [user@]hostname [command]
SSH can be used for port forwarding. The following command binds the 80 port of the remote computer to 8080 port of the local computer:
ssh -L 8080:remote_host_name:80 user@remote_host_name
-X flag enables X protocol forwarding from remote machine to local machine. So graphical programs can be run via SSH if -X flag was specified during connection.
Configuration files are located under /etc/ssh directory and ~/.ssh directory.

---
Telnet
Telnet is another program which allows to connect to remote machines.
Telnet doesn't support data encryption, therefore it is used only in local area networks.
Telnet provides a remote shell when connected to remote computer. Graphical programs can be configured to open their display on the client machine, so it is also possible to run programs with GUI through Telnet.
Usage:
telnet hostname [port]

---
VNC
Virtual Network Computing is a protocol which enables forwarding of screen, keyboard and mouse over network.
vncserver is a program which runs a desktop manager using virtual screen and allows clients to connect to that session over network.
vncviewer is a program which connects to vncserver and allows to view and/or control the session.

---
VNC continuation Managers
To set up a VNC session one should run vncserver with appropriate parameters:
vncserver :2 – there :2 is the number of display to use.
Note that the display used for VNC sessions is not bind to any tty, particularly it is impossible to view that display by pressing Alt+Ctrl+F7 (-F12).
To kill a VNC session use following command: vncserver -kill :2
Once the VNC session is started, clients can connect to it using following command: vncviewer host :display
Clients may be prompted for password, and depending on entered password may be granted view only or full access. The passwords for both cases are set up during first startup of VNC server, and can be changed using vncpasswd command

---
Instigate Training Center Foundation
134/1 Tsarav Aghbyur Str, Yerevan, 0054, Armenia
+374.60.510710
ggg.instigate.training